## Slide 2
Chapter 19
Basic Construction
Learning Objectives
List the primary styles of residential architecture.
Describe the major components of residential construction, including foundation systems, framing, walls, ceiling and roof, windows, insulation, interior finishes, and heating/cooling systems.
Describe government regulation of residential construction.

## Slide 3
Chapter 19
Basic House Construction
Architectural Types and Styles

## Slide 4
Basic Construction
Foundations
Footings
  most important building block of home
  supports foundation wall
  concrete base below frost line
Foundation Walls
  May be poured concrete, masonry or brick
Piers
  Additional structure built inside foundation walls

## Slide 5
Basic Construction
Framing

## Slide 6
Basic Construction
Framing
Framing is the wooden skeleton of the home.
See figure 19.2 and 19.3 in text
  Flooring
    Sill
    Flashing
    Girder
    Sheathing
    Joists
    trusses

## Slide 7
Basic Construction
Framing

## Slide 8
Basic Construction
Walls
Studs- Vertical framing
  2 by 4’s
  2 by 6’s
Ceiling Framing and Roof
ridge board
soffit
fascia
frieze board
eaves

## Slide 9
Basic Construction
Exterior Walls
R-Factor- resistance to heat transfer
  sheathing- strengthens walls
    plywood
    particle board
  siding- prevents water damage
    Aluminum, manufactured hardboard
    Vinyl, stucco, cement board
    Brick, wood
  weepholes

## Slide 10
Basic Construction
Windows
3 Types
Vertical Sliding (double hung)
Most common type in residential construction.
2. Swinging (Casement)
limit space (swing inward or outward)
do not insulate well
3. Fixed
picture, bay, bow

## Slide 11
Basic Construction
Doors
Interior
  wood or composite material
Exterior
  maximum insulation desired
  wood or steel
  high insulating core
Roofing
What type of materials are used in North Carolina?

## Slide 12
Basic Construction
Insulation
Primary purpose:
  resist flow of heat from one area to other
  prevents heating loss in winter
  protects against heat load in summer
  Used on ceiling, walls and floor
North Carolina Uniform Residential Building Code requirements for R-value:
  Walls- R-13
  Ceilings- R-30
  Floors- R-19

## Slide 13
Basic Construction
Moisture Control
Vapor barrier should be installed on inside wall side of insulation
Heating/Air Conditioning Systems (HVAC- Heating, Ventilation, Air Conditioning)
Central unit- only efficient system
  Gas- forced air or electric furnace?
  Heat pump
Efficiency and operating costs vary.
Agent must correctly identify type of HVAC system when listing or selling property.

## Slide 14
Basic Construction
Solar Heat
Passive or Active?
Provide only 50-60% of heat needed for home.
Electrical Systems
Note voltage of wiring, dedicated breakers and smoke detectors.

## Slide 15
Plumbing Systems
Adequacy and quality are important.
  Separate shut off valves
  Proper venting
  Size and insulation of water heater
Basic Construction

## Slide 16
Chapter 19
Basic Construction
Governmental Regulation
North Carolina Residential Building Code
Certificate of Occupancy
FHA/VA Minimum Standards
Contractor Licensing